## Slide 1: Bayesian Uncertainty Quantification of Physical Models in Thermal-Hydraulics System Codes
Damar Wicaksono (Thesis Directors: Prof. A. Pautz & Mr. O. Zerkak)
PhD Defense, EPF Lausanne, 19.01.2018

## Slide 2: Safety Analysis of LWR under LBLOCA: Show max. clad temperature < safety limit
Cold Leg
Hot Leg
Gas Phase
Liquid Phase
Double-ended
Guillotine Break
Emergency Core Cooling
Two-phase
hydraulics
Heat conduction through solids
Reactor Core
Reactor Pressure Vessel
ECC Mass Injection
Clad Temperature
Time
Safety Limit
Accumulator
Low Pressure Injection
Notes: Motivation: Safety Analysis of NPP under LBLOCA

## Slide 3: Forward Uncertainty Quantification: Uncertain Inputs Uncertain Outputs
Forward Model (Code)
Uncertain Inputs
(random variables)
Uncertain Outputs
Statistical Analysis of ``Quantities of Interest’’
Decision Making
Material properties
Initial conditions
Boundary conditions
Physical model parameters
Clad Temperature
Safety Limit
Safe/Fail, Accept/Reject, etc.
Monte Carlo simulation (multiple code runs)
e.g., PCT
Notes: This is statistical (probabilistic) framework

## Slide 4: Physical Model Parameters: post-Critical Heat Flux (CHF) Flow Regimes
pre-CHF
(Steam Convection)
Dispersed Flow Film Boiling (DFFB)
Interpolatory (Inverted Slug)
Inverted Annular Film Boiling (IAFB)
Transition Boiling
pre-CHF
(Nucleate Boiling)
Mass
Momentum
Energy
Closure Laws
Parametric
models
Notes: What are these physical model parameters?
Take for example the phenomenological models that describe two phase flow during a reflood of a dry channel
Closure laws describe the interaction between phases in each distinct **pre-determined** flow regime

## Slide 5: Uncertainty in Physical Model Parameters
FLECHT-SEASET
Westinghouse, USA
ACHILLES
Winfrith, UK
FEBA
KIT, Germany
Excerpt from the TRACE Code Theory Manual:
“…the approximate value of the coefficient in Eq. (4-119) was determined from data comparisons with FLECHT-SEASET high flooding rate reflood data…” (pp. 164)
“In TRACE, the above interfacial drag coefficient has been reduced by a factor of ¾ to better match FLECHT-SEASET high flooding rate reflood data, so…” (pp. 166)
RBHT
PSU, USA
What if the calibration was done on other, similar, separate effect test facilities (SETFs)?
Notes: Where is this uncertainty coming from

## Slide 6: Research Objectives
Given experimental data from a Separate Effect Test Facility (SETF), develop a methodology to:
Quantify the uncertainty of physical model parameters in a TH System Code
to be sampled from and propagated within statistical uncertainty analysis framework.
How to select important parameters to be inferred? Are the observed variables sensitive to change in the parameters?
How to approximate the input/output of the forward model? TRACE run takes time (minutes/run) and disk space (Mbytes/run).
How to make the inference (quantification)? How to obtain the PDF (or its approximation) of the parameters?
Is the quantified uncertainty useful? Is it applicable to make prediction?
Cast as a problem of statistical inference and entails four main questions:

## Slide 7: Scope of Research: Statistical Framework
How to select important parameters to be inferred? Are the observed variables sensitive to change in the parameters?
How to approximate the input/output of the forward model? TRACE run takes time (minutes) and disk space (MBytes).
How to make the inference (quantification)? How to obtain the PDF (or its approximation) of the parameters?
Is the quantified uncertainty useful? Is the quantified uncertainty applicable to make prediction?
Global Sensitivity Analysis
Gaussian Process Metamodeling
Bayesian Calibration
Uncertainty Propagation
Methods are non-intrusive
Methods require less assumptions about the underlying model
Ultimate results conform with probabilistic framework for UQ
Methods tend to be expensive
(require numerous code runs)
Notes: To answer those questions, we adapt and implement statistical methodologies derived from applied statistics especially related to the design and analysis of computer experiments.
This will also serve as the outline for the rest of the presentation we will start answering these questions one by one using a running example of TRACE model.
And we don’t develop codes, it is worthwhile to develop methods that is applied outside the code implementation.

## Slide 8: Scope of Research: FEBA Separate Effect Test Facility (SETF)
FEBA Reflood Tests were conducted at Kfz Karlsruhe (KIT) during 1980s for investigating bottom reflood using rod simulators (NiCr)
Three types of measurements were taken:
Clad temperature (8 axial locations)
Pressure drop (4 axial segments)
Liquid carryover
Main analyses are based on Test No. 216:
Notes: The method is adapted and demonstrated directly to solve this problem.
The problem is used in the OECD/NEA PREMIUM Benchmark

## Slide 9: Scope of Research: TRACE Model of FEBA SETF
Powered Heater Rods
Housing/Enclosure
Spacer grid
Inlet flow
Upper plenum
Backpressure
  (4) Experimental boundary conditions (, , etc.)
  (9) Material properties (etc.)
  (2) Spacer grid model ()
  (10) Post-CHF closure relations (IAFB wall , DFFB interfacial drag, etc.)
  (1) Quench temperature
  (1) Transition boiling
Model
parameters
Controllable inputs
27 Parameters are required to specify the model:
With flat independent prior uncertainties, either in linear or log scales
Notes: The method is adapted and demonstrated directly to solve this problem.
The problem is used in the OECD/NEA PREMIUM Benchmark

## Slide 10: Statistical Framework: Outline
Global Sensitivity Analysis
Gaussian Process Metamodeling
Bayesian Calibration
Uncertainty Propagation
How to approximate the input/output of the forward model?
How to make the inference (quantification)?
Is the quantified uncertainty useful?
27 initial parameters
(minutes/run)
(MBytes/run)
How to select important parameters to be inferred?
Clad Temperature [K]
Pressure Drop [bar]
Time [s]
Liquid Carryover [kg]
Which parameters are (not) influential?
For influential parameters, how parameters affect the output and by how much?
Propagation based on 1’000 samples
Notes: Uncertainty propagation using prior pdfs and 1’000 samples. Bands are constructed based on the 95% probability (2.5th – 97.5th percentile).

## Slide 11: Global Sensitivity Analysis for Screening: The Morris Screening Method
Elementary effect is the effect of a parameter perturbation on the output
Perturbation of one parameter at a time
Over many replications , the statistics of is a global sensitivity measure used in parameter importance ranking
Mean of absolute value
A complex model

## Slide 12: Global Sensitivity Analysis for Screening: The Morris Screening Method
Radial Scheme
Trajectory Scheme
Computation cost (Code runs)
# of parameters
Base / starting points
Perturbed points
Illustrations for 2 parameters and 4 replications
Over many replications , the statistics of is a global sensitivity measure
Notes: The idea of global method is that we don’t use many assumptions regarding the input/output hyper-surface. Perturbation from one point might give different results compared to the perturbation from another point.
We evaluate the input over range that is wide that might cause departure from a well behaved response
But Morris is qualitative (ordinal) does not intuitively tell how important a parameter is.

## Slide 13: Global Sensitivity Analysis for Screening: Sobol’ Total-Effect Indices
Written in integral form:
Computed by Monte Carlo estimation with cost (code runs):
# of parameters
N = 1’000 | # of parameters () |  | 
Code runs |  |  | 
N = 1’000 |  |  | 
Code runs |  |  | 
Output variance left if all parameters except are fixed. If small then is less influential and can be fixed.
Sobol’ total-effect index for parameter :
(-dimension

## Slide 14: Global Sensitivity Analysis for Screening: Comparison of Methods
Sensitivity Measure
Number of Replications / Samples
replications runs
samples runs
Selected Quantity of Interest: Time-Average Output
Boundary conditions, closure laws, and spacer grid model parameters are relatively influential (12 parameters) based on total-effect indices cut-off
Notes: The three screening methods give (more/less) consistent ranking
But you don’t actually need to run all the way through

## Slide 15: Uncertainty Propagation using Influential vs. Non-Influential Parameters
Clad Temperature [K]
Pressure Drop [bar]
Time [s]
Liquid Carryover [kg]
12 Influential
15 Non-influential
Parameter subsets
Uncertainty propagation using 2 parameter subsets and 500 Monte Carlo samples

## Slide 16: Statistical Framework: Outline
Global Sensitivity Analysis
Gaussian Process Metamodeling
How to select important parameters to be inferred?
How to approximate the input/output of the forward model?
27 initial parameters
12 influential parameters
Construct a metamodel for fast and efficient approximation

## Slide 17: Gaussian Process Metamodel
Prior
Data
Posterior
Probability distribution of functions
mean function
process variance
correlation (kernel) function
e.g., power-exponential correlation, a 2-parameter function
Gaussian Process
Gaussian process is a Gaussian with continuous variates:
Application in Regression
Notes: If we fit the hyper-parameters we can use it to make prediction on location of x not observed
As a regression tool it is no

## Slide 18: Dealing with Multivariate Output: Principal Component Analysis
Output of the TRACE model of FEBA is highly multivariate.
Output Type | # of outputs
Clad Temperature | 
Pressure Drop | 
Liquid Carryover | 
Output Type | 
Clad Temperature | 
Pressure Drop | 
Liquid Carryover | 
Dimension reduction by Principal Component Analysis (PCA)
SVD
Concatenate and centered outputs
Eigenvectors (principal components)
PC scores
PC scores as function of input parameters predicted by GP
the mean of output
Mean and 1st PC of clad temperature output
Prediction of multivariate output

## Slide 19: Constructing GP Metamodel

## Slide 20: The training sample size is the main factor for the metamodel performance
Covariance Kernel Functions
Design of Experiment
Training Sample Size
Major impact
Minor impact
Negligible impact

## Slide 21: Testing the Trained Metamodel () on the Testing Samples ()
Observed Rec. Error [K]
Predicted Rec. Error [K]
Predicted Rec. Error [Pa]
Observed Rec. Error [Pa]
Observed Rec. Error [kg]
Predicted Rec. Error [kg]
Clad Temperature
Pressure Drop
Liquid Carryover
GP RMSE
Test Data
Acceptable metamodel predictive performance based on the testing samples
Notes: The metamodel prediction is limited by the error due to dimension reduction
It also shows that we cannot go better than the error given by the metamodel.
In context it is find for the time being as the prior uncertainty gives a larger error (standard deviation)

## Slide 22: Statistical Framework: Outline
Global Sensitivity Analysis
Gaussian Process Metamodeling
Bayesian Calibration
How to select important parameters to be inferred?
How to approximate the input/output of the forward model?
How to make the inference (quantification)?
27 initial parameters
12 influential parameters
Wide, independent prior uncertainties
Use experimental data to constrain the prior

## Slide 23: Bayesian Calibration, Inverse Quantification: Uncertain (Inputs + Data) Uncertain Inputs Updated
Forward Model
Uncertain model parameters (posterior)
Likelihood
Experimental Data from SETF
Additional sources of uncertainty
Uncertain model parameters (prior)
Controllable inputs (w.r.t experiment)
Probability of observing data given parameters
Bayes’
Theorem

## Slide 24: Two Aspects of Bayesian Calibration: Formulation and Computation
Forward Model
Uncertain model parameters (posterior)
Likelihood
Experimental Data from SETF
Additional sources of uncertainty
Uncertain model parameters (prior)
Controllable inputs (w.r.t experiment)
Formulation
Computation

## Slide 25: Formulation of Bayesian Calibration: True, Measured, and Predicted Values
Model Discrepancy, unknown
Experimental Data is a distorted information of the true value
Model prediction is a distorted information of the true value
Controlled/Design Variables, known (e.g., pressure, heat flux, etc.)
spatio-temporal process, multi-dimensional, correlated
Measurement error, random
Computer Model, expensive to run
Given and other unknowns, what is and its uncertainties?

## Slide 26: Normal Likelihood and Flat Prior: Posterior Formulation
GP meta-model
Principal Comp. truncation
model discrepancy
experiment and other
Multiple sources of variance, avoid overfitting
Likelihood
Gaussian
Gaussian
Gaussian
given
unknown
Consider only data from 1 FEBA Test. No in formulation

## Slide 27: Computation of Bayesian Calibration
Bayes’ Theorem
Posterior
Normalization constant, multi-D integral, not necessary with MCMC
Likelihood
Prior
The Metropolis-Hastings (MH) Algorithm to sample from an un-normalized density , in a nutshell*:
Start at any random value
Generate sample close to the current value
Accept or reject based on

## Slide 28: Setup for Calibration Simulations

## Slide 29: Visualizing Multi-dimensional Posterior: How to read a corner plot?
Parameter 1
Parameter 2
Parameter 3
Parameter 4
Parameter 5
Parameter 1
Parameter 2
Parameter 3
Parameter 4
Parameter 5

## Slide 30: Visualizing Multi-dimensional Posterior: How to read a corner plot?
Bivariate Marginals
Projection into one axis
Visualize the uncertainty of a parameter
Joint plot of two parameters
Visualize pairwise correlations
Lighter color = high concent. of samples
Parameter 1
Parameter 2
Parameter 3
Parameter 4
Univariate Marginals
Parameter 5

## Slide 31: Constraining the Prior Uncertainty Range of the Model Parameters
gridHT
iafbWHT
dffbWHT
dffbVIHT
iafbIntDr
dffbIntDr
dffbWDr
tQuench
The prior uncertainty of the model parameters
(samples)
Notes: Can the data and the calibration model can be used to constrain this prior?

## Slide 32: Results: Considering multiple types of data helps constrain the parameters uncertainty
gridHT
iafbWHT
dffbWHT
dffbVIHT
iafbIntDr
dffbIntDr
dffbWDr
tQuench
The posterior based on pressure drop data only
(samples)
Notes: The vertical lines in the diagonal is the 95% credible interval

## Slide 33: Results: Considering multiple types of data helps constrain the parameters uncertainty
gridHT
iafbWHT
dffbWHT
dffbVIHT
iafbIntDr
dffbIntDr
dffbWDr
tQuench
The posterior based on all types of data
(samples)
Notes: Data can help constrain the prior range of the model parameters.
But the posterior samples also exhibit correlation among the parameters

## Slide 34: Results: Posterior Samples are Correlated (i.e., a set of “collectively-fitted” values)
Time [s]
Clad Temperature [K]
Middle assembly
Top assembly
Uncertainty propagation on FEBA Test. No. 216 (the calibration data) based on 1’000 Monte Carlo samples.
Prior
Posterior, Correlated
Posterior, Independent
Notes: A set of “collectively-fitted” values which means that if we don’t consider them as a collection then the prediction would less match the calibration data itself.
If we only consider the univariate marginals (neglecting correlation) we obtain prediction that is less consistent with the calibration data.
Only if we consider the posterior samples jointly, that the prediction match the experimental data better.

## Slide 35: Results: Posterior without Model Bias Term Some nominal parameter are outside 95% CIs*
gridHT
iafbWHT
dffbWHT
dffbVHT
iafbIntDr
dffbIntDr
dffbWDr
tQuench
Calibration using all types of data, w/o Model Bias Term
*Credible intervals

## Slide 36: Results: Calibration without Model Bias Term Uncertainty propagation on FEBA Test No. 216
Time [s]
Clad Temperature [K]
Time [s]
Liquid Carryover [kg]
Significant effect at the top of the assembly
Allowing large change to parameters improve prediction on the liquid carryover
Prior
Posterior, Correlated
Posterior, Independent
Middle assembly
Top assembly
Notes: Large change relative to the nominal parameter value

## Slide 37: Statistical Framework: Outline
Global Sensitivity Analysis
Gaussian Process Metamodeling
Bayesian Calibration
How to select important parameters to be inferred?
How to approximate the input/output of the forward model?
How to make the inference (quantification)?
Is the quantified uncertainty useful?
27 initial parameters
12 influential parameters
Wide, independent prior uncertainties
Narrower, correlated posterior uncertainties
Uncertainty Propagation
Wide prior prediction uncertainties
Propagate posterior uncertainties for different experimental conditions

## Slide 38: Comparing Different Calibration Results: Informativeness vs. Calibration Score
Two scores to summarize and compare results of uncertainty propagation using different posterior samples w.r.t to the prior
LUB: Lower Uncertainty Bound
( prediction percentile)
( prediction percentile)
UUB: Upper Uncertainty Bound
Informativeness for output
Posterior prediction uncertainty is equal to that of the prior
No posterior prediction uncertainty
Notes: Think of a posterior prediction is a source of information for output y and defined only in three values, the lower uncertainty bound, the upper uncertainty bound and the reference value
Informativeness tries to measure the width of posterior uncertainty band relative to that of the prior

## Slide 39: Comparing Different Calibration Results: Informativeness vs. Calibration Score
Two scores to summarize and compare results of uncertainty propagation using different posterior samples w.r.t to the prior
Calibration Score for output
Experimental data falls outside the uncertainty band
Experimental data matches the reference value exactly
The height of the experimental data in the information triangle
: Reference value
( prediction percentile; median)
Notes: Calibration measure the location of experimental data inside the so called “information” triangle

## Slide 40: Posterior Uncertainties are More Informative but can be Much Less “calibrated”
  ,
Calibration Score [-]
  ,
  ,
  ,
  ,
Informativeness [-]
Calibration Scheme
Notes: Across experimental conditions there is no strong pattern of discrepancy
Less “calibrated” here means cover less experimental data points
For posterior with model bias term, there is large different in both scores when excluding correlation

## Slide 41: Removing Highly Correlated Parameter and Keeping it at Prior Range Give a Compromise
  ,
Informativeness [-]
Calibration Score [-]
  ,
  ,
  ,
  ,
Calibration Scheme
Notes: So there is reason to be prudent when it comes to correlation. (univariate marginal) Parameter uncertainty can be wide (indicating no overfitting) but the correlation can cause such overfitting nevertheless.

## Slide 42: Conclusion
How to select important parameters to be inferred?
How to approximate the input/output of the forward model?
How to make the inference (quantification)?
Is the quantified uncertainty useful?

## Slide 43: Conclusion: Demonstration of the Methodology on the FEBA TRACE Model
Global Sensitivity Analysis
Gaussian Process Metamodeling
Bayesian Calibration
How to select important parameters to be inferred?
How to approximate the input/output of the forward model?
How to make the inference (quantification)?
Is the quantified uncertainty useful?
27 initial parameters
12 influential parameters
Wide, independent prior uncertainties
Narrower, correlated posterior uncertainties
Uncertainty Propagation
Narrower posterior prediction uncertainties for all exp. conditions
Wide prior prediction uncertainties

## Slide 44: Future Work

## Slide 45: Future Work

## Slide 46: Wir schaffen Wissen – heute für morgen
Thank you for your attention.
My sincere gratitude to:
Prof. A. Pautz
Mr. O. Zerkak
Dr. G. Perret
Mr. Ph. Jacquemoud
Dr. M. Hursin
Dr. D. Rochman
Mr. H. Ferroukhi
Other members of STARS
The jury members:
Dr. J. Baccou
Prof. R. Houdré
Prof. B. Sudret
Dr. W. Zwermann
Additional acknowledgments:
Swiss Federal Nuclear Safety Inspectorat (ENSI)
Swiss Federal Office of Energy (BFM)

## Slide 47: Uncertainty in Physical Model Parameters
Notes: Where is this uncertainty coming from

## Slide 48: Main Results: Considering multiple types of data helps constrain the parameters uncertainty
gridHT
iafbWHT
dffbWHT
dffbVIHT
iafbIntDr
dffbIntDr
dffbWDr
tQuench
The posterior based on clad temperature data only
(samples)

## Slide 49: Main Results: Considering multiple types of data helps constrain the parameters uncertainty
gridHT
iafbWHT
dffbWHT
dffbVIHT
iafbIntDr
dffbIntDr
dffbWDr
tQuench
The posterior based on liquid carryover data only
(samples)

## Slide 50: Main Results: Calibration excluding strongly correlated parameter
gridHT
iafbWHT
dffbWHT
iafbIntDr
dffbIntDr
dffbWDr
tQuench
The posterior without a strongly correlated parameter, dffbVIHT
(samples)