## Slide 1: Bayesian Uncertainty Quantification of Physical Models in Thermal-Hydraulics System Codes
Damar Wicaksono (Thesis Directors: Prof. A. Pautz & Mr. O. Zerkak)
PhD Defense, EPF Lausanne, 19.01.2018

## Slide 2: Safety Analysis of LWR under LBLOCA: Show max. clad temperature < safety limit
Cold Leg
Hot Leg
Gas Phase
Liquid Phase
Double-ended
Guillotine Break
Emergency Core Cooling
Two-phase
hydraulics
Heat conduction through solids
Reactor Core
Reactor Pressure Vessel
ECC Mass Injection
Clad Temperature
Time
Safety Limit
Accumulator
Low Pressure Injection
Notes: Motivation: Safety Analysis of NPP under LBLOCA

## Slide 3: Forward Uncertainty Quantification: Uncertain Inputs Uncertain Outputs
Forward Model (Code)
Uncertain Inputs
(random variables)
Uncertain Outputs
Statistical Analysis of ``Quantities of Interest’’
Decision Making
Material properties
Initial conditions
Boundary conditions
Physical model parameters
Clad Temperature
Safety Limit
Safe/Fail, Accept/Reject, etc.
Monte Carlo simulation (multiple code runs)
e.g., PCT
Notes: This is statistical (probabilistic) framework

## Slide 4: Physical Model Parameters: post-Critical Heat Flux (CHF) Flow Regimes
pre-CHF
(Steam Convection)
Dispersed Flow Film Boiling (DFFB)
Interpolatory (Inverted Slug)
Inverted Annular Film Boiling (IAFB)
Transition Boiling
pre-CHF
(Nucleate Boiling)
Mass
Momentum
Energy
Closure Laws
Parametric
models
Notes: What are these physical model parameters?
Take for example the phenomenological models that describe two phase flow during a reflood of a dry channel
Closure laws describe the interaction between phases in each distinct **pre-determined** flow regime

## Slide 5: Uncertainty in Physical Model Parameters
FLECHT-SEASET
Westinghouse, USA
ACHILLES
Winfrith, UK
FEBA
KIT, Germany
Excerpt from the TRACE Code Theory Manual:
“…the approximate value of the coefficient in Eq. (4-119) was determined from data comparisons with FLECHT-SEASET high flooding rate reflood data…” (pp. 164)
“In TRACE, the above interfacial drag coefficient has been reduced by a factor of ¾ to better match FLECHT-SEASET high flooding rate reflood data, so…” (pp. 166)
RBHT
PSU, USA
What if the calibration was done on other, similar, separate effect test facilities (SETFs)?

## Slide 6: Inverse Uncertainty Quantification: Uncertain (Inputs+Data) Uncertain Inputs Updated
Forward Model
Uncertain model parameters (posterior)
Likelihood
Experimental Data from SETF
Additional sources of uncertainty
Uncertain model parameters (prior)
Controllable inputs (w.r.t experiment)
Probability of observing data given parameters
Bayes’
Theorem

## Slide 7: Research Objectives
Given experimental data from a Separate Effect Test Facility (SETF), develop a methodology to:
Quantify the uncertainty of physical model parameters in a TH System Code
to be sampled from and propagated within statistical uncertainty analysis framework.
How to select important parameters to be inferred? Are the observed variables sensitive to change in the parameters?
How to approximate the input/output of the forward model? TRACE run takes time (minutes/run) and disk space (Mbytes/run).
How to make the inference (quantification)? How to obtain the PDF (or its approximation) of the parameters?
Is the quantified uncertainty useful? Is it applicable to make prediction?
Cast as a problem of statistical inference and entails four main questions:

## Slide 8: Scope of Research: Statistical Framework
How to select important parameters to be inferred? Are the observed variables sensitive to change in the parameters?
How to approximate the input/output of the forward model? TRACE run takes time (minutes) and disk space (MBytes).
How to make the inference (quantification)? How to obtain the PDF (or its approximation) of the parameters?
Is the quantified uncertainty useful? Is the quantified uncertainty applicable to make prediction?
Global Sensitivity Analysis
Gaussian Process Metamodeling
Bayesian Calibration
Uncertainty Propagation
Methods are non-intrusive
Methods require less assumptions about the underlying model
Ultimate results conform with probabilistic framework for UQ
Methods tends to be expensive (require numerous code runs)
Notes: To answer those questions, we adapt and implement statistical methodologies derived from applied statistics especially related to the design and analysis of computer experiments.
This will also serve as the outline for the rest of the presentation we will start answering these questions one by one using a running example of TRACE model.
And we don’t develop codes, it is worthwhile to develop methods that is applied outside the code implementation.

## Slide 9: Scope of Research: TRACE Model of FEBA Separate Effect Test Fac.
Powered Heater Rods
Housing/Enclosure
Spacer grid
Inlet flow
Upper plenum
Backpressure
  (4) Experimental boundary conditions (backpressure, inlet flow, etc.)
  (9) Material properties (conductivity, heat capacity, etc.)
  (2) Spacer grid model (HTC enhancement, pressure drop effect)
  (10) Post-CHF closure relations (IAFB wall HTC, DFFB interfacial drag, etc.)
  (1) Quench temperature
  (1) Transition boiling HTC
Model
parameters
Controllable inputs
27 Parameters are required to specify the model:
Notes: The method is adapted and demonstrated directly to solve this problem.
The problem is used in the OECD/NEA PREMIUM Benchmark

## Slide 10: Global Sensitivity Analysis

## Slide 11: The training sample size is the main factor for the metamodel performance
Design of Experiment
Training Sample Size
Minor impact
Negligible impact
Major impact

## Slide 12: Design Requirements for Your Presentation
The PSI has a new layout for PowerPoint presentations. Please use this template for new presentations.
Tip:
If you intend to copy text from other sources into this PowerPoint template, please proceed as follows in order for the copied text to appear in the Calibri font: instead of inserting the text with Ctrl+v to the place where you would like it to appear, click on the right-hand mouse button at this spot. A drop-down menu will appear with the menu item paste options. You will find several tiles below. One is marked with a capital A. Click on this tile and your copied text will be inserted in the Calibri font. Please note: text formatting like bold and italics will not be transferred. This is due to the programme properties of PowerPoint, which cannot be overridden by the creators of this PowerPoint template.

## Slide 13: Design Requirements for Your Presentation
Please create your slides exclusively according to the following requirements:
Slide title: Georgia normal, font size 25, colour dark grey. You may not use any other logos in the slide title.
Logo: The PSI-logo may not be altered/added to
Sub title: Calibri bold
Running text: Calibri, font size not smaller than 16.
Font colours: black and white, dark grey for the title of the presentation. You can write in bold, only use italics when citing literature. Please do without underlining and shadowing.
In an English PowerPoint presentation all textual information should be given in English, including the texts in graphs and photos.
Colours: If possible use the «user-defined colurs» you find below the tile
  or those from the slide «PSI colour scheme» for your graphs. Brightness grades are permitted for colours.
Please note that the German language motto of «Wir schaffen Wissen – heute für morgen» is not translated and remains in German on the title slide. A complimentary translation would sound something like «We create knowledge today – for use tomorrow»
The grey background as you see it on this slide is an option.

## Slide 14: Example Slide with Two Columns
Example text agnatet excepeliqui di aceruptat aut lat es dis aut expelecum eliam etus explatem.
  unda non eaque nis dolupta epudam, odis acepraerum fugita venitat eat rem ullenistiat
    aditis repre que nihic tem rae voluptatenis quod qui aceris restibus
Example text agnatet excepeliqui di aceruptat aut lat es dis aut expelecum eliam etus explatem.
  unda non eaque nis dolupta epudam, odis acepraerum fugita venitat eat rem ullenistiat
    aditis repre que nihic tem rae voluptatenis quod qui aceris restibus

## Slide 15: Example Slide with Two Columns and Grey Background
Example text agnatet excepeliqui di aceruptat aut lat es dis aut expelecum eliam etus explatem.
  unda non eaque nis dolupta epudam, odis acepraerum fugita venitat eat rem ullenistiat
    aditis repre que nihic tem rae voluptatenis quod qui aceris restibus
Example text agnatet excepeliqui di aceruptat aut lat es dis aut expelecum eliam etus explatem.
  unda non eaque nis dolupta epudam, odis acepraerum fugita venitat eat rem ullenistiat
    aditis repre que nihic tem rae voluptatenis quod qui aceris restibus

## Slide 16: PSI Colour Scheme
Colour options for graphs: 1st choice
Colour options for graphs: 2nd choice
PSI‘s basic colours

## Slide 17: Wir schaffen Wissen – heute für morgen
This is an example of a summary on a final slide: at PSI we use synchrotron light to look into magnetic materials and thus …
… understand the details of the nanoworld in order to optimise technology.
  … understand the interaction between new materials.
  … maybe discover new nanomagnets.

## Slide 18: Wir schaffen Wissen – heute für morgen
Thank you for your attention.
My sincere gratitude to:
Prof. A. Pautz
Mr. O. Zerkak
Dr. G. Perret
Mr. Ph. Jacquemoud
Dr. M. Hursin
Dr. D. Rochman
Mr. H. Ferroukhi
Other members of STARS
The jury members:
Prof. R. Houdré
Dr. J. Baccou
Dr. W. Zwermann
Prof. B. Sudret
Additional acknowledgments:
Swiss Federal Nuclear Safety Inspectorat (ENSI)
Swiss Federal Office of Energy (BFM)

## Slide 19: ETHZ-EPFL MSc in Nuclear Engineering
Swiss joint MSc program between ETHZ and EPFL
Established in 2008, more than 100 students
Two-year program, 120 ECTS credits
Students attend two top-ranked universities:
  ETH Zurich #9
  EPF Lausanne #14 (based on QS)
Scientific support and research at the Paul Scherrer Institute
Grants and scholarships available
Notes: The Swiss Master of Science in Nuclear Engineering program is the only joint program between the Swiss Federal Institutes of Technology in Zurich and Lausanne (ETHZ and EPFL).
It was created in 2008 and after 8 years more than 100 students have successfully attended the master program.
The program lasts two years (equivalent to 120 European Credit Transfer & Accumulation System credits), and the students attend two of the best universities with world-wide reputation; ETHZ which ranks at the 9th position and the EPFL which ranks on the 14th position based on the QS university ranking system for 2016.
The students receive a continuous strong scientific support from top level scientists of the Paul Scherrer Institute (the Swiss federal multi-disciplinary research center for natural sciences and technology).
Numerous scholarships, accommodation & travel grants and allowances are available for the students. For example, all students have in the past received mobility grants.
On the right hand side pictures you can see (from top to bottom) the legendary central building of ETH in Zurich, the innovative campus of EPFL with the Rolex Learning Center next to the Geneva lake, and the traditional Swiss landscape where the PSI is located alongside the Aare river.
The central picture shows the location of EPFL, ETHZ and PSI on the map of Switzerland, right in the heart of Europe.

## Slide 20: ETHZ-EPFL MSc in Nuclear Engineering
Curriculum focuses on:
Neutronics
Thermohydraulics
Nuclear Material Science
Nuclear Safety
Waste Management
Radiation Protection
  …and more
Unique world-class facilities:
CROCUS research reactor
Swiss Light Source synchrotron
Hot Lab facility
Proton therapy center
Numerous TH experimental facilities
Curriculum includes:
Three-month industrial internship
Research project
Master thesis
Notes: The curriculum of the Swiss Master Program in Nuclear Engineering covers many areas of Nuclear Engineering. A plethora of courses in neutronics, thermohydraulics, nuclear material science, nuclear safety, waste management, radiation protection and others, are provided and taught by top level Professors and scientists from EPFL, ETHZ and PSI.
The students have the opportunity to get trained and perform hands-on work on unique world-class facilities, like:
  the CROCUS zero power education and research reactor at EPFL.
  the Swiss Light Source (SLS) at PSI, a 3rd generation synchrotron light source with an energy 2.4 GeV which provides photon beams of high brightness for research in materials science, biology and chemistry.
  the Hot Lab facility, the only Swiss laboratory authorized by the safety authorities to handle large quantities of radioactive materials including commercial as well as experimental nuclear fuel.
  the Proton Therapy Center at PSI, the worldwide first compact scanning gantry for the irradiation of deep-seated tumors with proton beam.
  numerous Thermohydraulic facilities at ETHZ and PSI, focusing on fast neutron imaging, large scale investigation of natural circulation, bubble experiments, aerosol generation, etc.
  and others.
Finally during the last year of the studies, the students have to perform
  a 3-month internship at the Swiss nuclear industry [nuclear power plants (KKG, KKL, KKB, KKM), nuclear utilities (Axpo, Alpic, BKW, etc.), regulatory body (ENSI), etc.]. Students have the possibility to do their internship also abroad.
  a research project at PSI and a 6-month master thesis project (at PSI, ETH, EPFL, or in industry) which complete the curriculum.

## Slide 21: ETHZ-EPFL MSc in Nuclear Engineering
For more information visit master-nuclear.ch
Notes: For the first 8 years of the master program, more than 100 students have followed nuclear engineering studies in Switzerland.
The program has a very international character, with the students coming from 30 different countries across the globe, and from 44 different universities.
  the majority of the students come from France (15%), China (14%) and Switzerland (10%).
The structure of the program receives a very positive feedback, as 94% of the students have stated that they are (very) satisfied with the program.
After their graduation, 83% of the graduates remain in the nuclear field and 62% of the graduates continue their career in Switzerland.
Finally, it is worth noting that both ETHZ and EPFL have very low tuition fees (600 euros per semester) for all students (Swiss and non-Swiss).
For more information you can visit the official web-site of the master program (master-nuclear.ch)