## Slide 1: Bayesian Uncertainty Quantification of Physical Models in Thermal-Hydraulics System Codes
Damar Wicaksono (Thesis Directors: Prof. A. Pautz & Mr. O. Zerkak)
PhD Defense, EPF Lausanne, 19.01.2018

## Slide 2: Safety Analysis of LWR under LBLOCA: Show max. clad temperature < safety limit
Cold Leg
Hot Leg
Gas Phase
Liquid Phase
Double-ended
Guillotine Break
Emergency Core Cooling
Two-phase
hydraulics
Heat conduction through solids
Reactor Core
Reactor Pressure Vessel
ECC Mass Injection
Clad Temperature
Time
Safety Limit
Accumulator
Low Pressure Injection
Notes: To put things into context let’s revisit the role of simulation in the safety analysis of NPP, in this case under LBLOCA in perhaps rather simplistic view.
We make prediction whether some safety criteria is within the safety limit.
Simulation is based on the simulation of the two phase flow in the coolant circuit.

## Slide 3: Forward Uncertainty Quantification: Uncertain Inputs Uncertain Outputs
Forward Model (Code)
Uncertain Inputs
(random variables)
Uncertain Outputs
Statistical Analysis of ``Quantities of Interest’’
Decision Making
Material properties
Initial conditions
Boundary conditions
Physical model parameters
Clad Temperature
Safety Limit
Safe/Fail, Accept/Reject, etc.
Monte Carlo simulation (multiple code runs)
e.g., PCT
Notes: This is statistical (probabilistic) framework

## Slide 4: Physical Model Parameters: post-Critical Heat Flux (CHF) Flow Regimes
pre-CHF
(Steam Convection)
Dispersed Flow Film Boiling (DFFB)
Interpolatory (Inverted Slug)
Inverted Annular Film Boiling (IAFB)
Transition Boiling
pre-CHF
(Nucleate Boiling)
Mass
Momentum
Energy
Closure Laws
Parametric
models
Notes: What are these physical model parameters?
Take for example the phenomenological models that describe two phase flow during a reflood of a dry channel
Closure laws describe the interaction between phases in each distinct **pre-determined** flow regime
Here is system code TRACE

## Slide 5: Uncertainty in Physical Model Parameters
FLECHT-SEASET
Westinghouse, USA
ACHILLES
Winfrith, UK
FEBA
KIT, Germany
Excerpt from the TRACE Code Theory Manual:
“…the approximate value of the coefficient in Eq. (4-119) was determined from data comparisons with FLECHT-SEASET high flooding rate reflood data…” (pp. 164)
“In TRACE, the above interfacial drag coefficient has been reduced by a factor of ¾ to better match FLECHT-SEASET high flooding rate reflood data, so…” (pp. 166)
RBHT
PSU, USA
What if the calibration was done on other, similar, separate effect test facilities (SETFs)?
Notes: Where is this uncertainty coming from

## Slide 6: Research Objectives
Given experimental data from a Separate Effect Test Facility (SETF), develop a methodology to:
quantify the uncertainty of physical model parameters in a TH System Code
to be sampled from and propagated within statistical uncertainty analysis framework.
How to select important parameters to be inferred? Are the observed variables sensitive to change in the parameters?
How to approximate the input/output of the forward model? TRACE run takes time (minutes/run) and disk space (Mbytes/run).
How to make the inference (quantification)? How to obtain the PDF (or its approximation) of the parameters?
Is the quantified uncertainty useful? Is it applicable to make prediction?
In an illustrative example this entails four main questions:

## Slide 7: Scope of Research: Statistical Framework
How to select important parameters to be inferred? Are the observed variables sensitive to change in the parameters?
How to approximate the input/output of the forward model? TRACE run takes time (minutes) and disk space (MBytes).
How to make the inference (quantification)? How to obtain the PDF (or its approximation) of the parameters?
Is the quantified uncertainty useful? Is the quantified uncertainty applicable to make prediction?
Global Sensitivity Analysis
Gaussian Process Metamodeling
Bayesian Calibration
Uncertainty Propagation
Methods are non-intrusive
Methods require less assumptions about the underlying model
Ultimate results conform with probabilistic framework for UQ
Methods tend to be expensive
(require numerous code runs)
Notes: To answer those questions, we adapt and implement statistical methodologies derived from applied statistics especially related to the design and analysis of computer experiments.
This will also serve as the outline for the rest of the presentation we will start answering these questions one by one using a running example of TRACE model.
And we don’t develop codes, it is worthwhile to develop methods that is applied outside the code implementation.

## Slide 8: Scope of Research: FEBA Separate Effect Test Facility (SETF)
FEBA Reflood Tests were conducted at Kfz Karlsruhe (KIT) during 1980s for investigating bottom reflood using rod simulators (NiCr)
Three types of measurements were taken:
Clad temperature (8 axial locations)
Pressure drop (4 axial segments)
Liquid carryover
Main analyses are based on Test No. 216:
Notes: The method is adapted and demonstrated directly to solve this problem.
The problem is used in the OECD/NEA PREMIUM Benchmark

## Slide 9: Scope of Research: TRACE Model of FEBA SETF
Powered Heater Rods
Housing/Enclosure
Spacer grid
Inlet flow
Upper plenum
Backpressure
  (4) Experimental boundary conditions (, , etc.)
  (9) Material properties (etc.)
  (2) Spacer grid model ()
  (10) Post-CHF closure relations (IAFB wall , DFFB interfacial drag, etc.)
  (1) Quench temperature
  (1) Transition boiling
Model
parameters
Controllable inputs
27 Parameters are required to specify the model:
With flat independent uncertainties, either in linear or log scales
Notes: The method is adapted and demonstrated directly to solve this problem.
The problem is used in the OECD/NEA PREMIUM Benchmark

## Slide 10: Statistical Framework: Outline
Global Sensitivity Analysis
Gaussian Process Metamodeling
Bayesian Calibration
Uncertainty Propagation
How to approximate the input/output of the forward model?
How to make the inference (quantification)?
Is the quantified uncertainty useful?
27 initial parameters
(minutes/run)
(MBytes/run)
How to select important parameters to be inferred?
Clad Temperature [K]
Pressure Drop [bar]
Time [s]
Liquid Carryover [kg]
Which parameters are (not) influential?
For influential parameters, how parameters affect the output and by how much?
Propagation based on 1’000 samples
Notes: Uncertainty propagation using prior pdfs and 1’000 samples. Bands are constructed based on the 95% probability (2.5th – 97.5th percentile).

## Slide 11: Global Sensitivity Analysis for Screening: The Morris Screening Method
Elementary effect is the effect of a parameter perturbation on the output
Perturbation of one parameter at a time
Over many replications , the statistics of is a global sensitivity measure used in parameter importance ranking
Mean of absolute value
A complex model

## Slide 12: Global Sensitivity Analysis for Screening: The Morris Screening Method
Radial Scheme
Trajectory Scheme
Computation cost (Code runs)
# of parameters
Base / starting points
Perturbed points
Illustrations for 2 parameters and 4 replications
Over many replications , the statistics of is a global sensitivity measure
Notes: The idea of global method is that we don’t use many assumptions regarding the input/output hyper-surface. Perturbation from one point might give different results compared to the perturbation from another point.
We evaluate the input over range that is wide that might cause departure from a well behaved response
But Morris is qualitative (ordinal) does not intuitively tell how important a parameter is.

## Slide 13: Global Sensitivity Analysis for Screening: Sobol’ Total-Effect Indices
Written in integral form:
Computed by Monte Carlo estimation with cost (code runs):
# of parameters
Output variance left if all parameters except are fixed. If small then is less influential and can be fixed.
Sobol’ total-effect index for parameter :
(-dimension

## Slide 14: Global Sensitivity Analysis for Screening: Comparison of Methods
Sensitivity Measure
Number of Replications / Samples
replications runs
samples runs
Selected Quantity of Interest: Time-Average Output
Boundary conditions, closure laws, and spacer grid model parameters are relatively influential (12 parameters) based on total-effect indices cut-off
Results on TC4 output
Notes: The three screening methods give (more/less) consistent ranking
Quite a lot of run required but maybe you don’t actually need to run all the way through

## Slide 15: Uncertainty Propagation using Influential vs. Non-Influential Parameters
Clad Temperature [K]
Pressure Drop [bar]
Time [s]
Liquid Carryover [kg]
12 Influential
15 Non-influential
Parameter subsets
Uncertainty propagation using 2 parameter subsets and 500 Monte Carlo samples

## Slide 16: Statistical Framework: Outline
Global Sensitivity Analysis
Gaussian Process Metamodeling
How to select important parameters to be inferred?
How to approximate the input/output of the forward model?
27 initial parameters
12 influential parameters
Construct a metamodel for fast and efficient approximation
Metamodel = a model of a model

## Slide 17: Gaussian Process (GP) Metamodel
Prior
Data
Posterior
Probability distribution of functions
mean function
process variance
correlation (kernel) function
e.g., power-exponential correlation, a 2-parameter function
Gaussian Process
Gaussian process is a Gaussian with continuous variates:
Application in Regression
Notes: If we fit the hyper-parameters we can use it to make prediction on location of x not observed
As a regression tool it is no

## Slide 18: Constructing GP Metamodel: Training and Testing
Validation/Testing
Design of Experiment
Training Runs
Validation/Testing Runs
Model fitting
Different training sample sizes
Different design schemes
Different covariance kernels
Different factors involved in the construction of GP Metamodel
Prediction of validation/testing runs

## Slide 19: Dealing with Multivariate Output: Principal Component Analysis
Output of the TRACE model of FEBA is highly multivariate.
Output Type | # of outputs
Clad Temperature | 
Pressure Drop | 
Liquid Carryover | 
Output Type | 
Clad Temperature | 
Pressure Drop | 
Liquid Carryover | 
Dimension reduction by Principal Component Analysis (PCA)
SVD
Concatenate and centered outputs
Eigenvectors (principal components)
PC scores
PC scores as function of input parameters predicted by GP
the mean of output
Mean and 1st PC of clad temperature output
Prediction of multivariate output
Notes: Note that Q is the number of retained principal components used to reconstruct the full output space and it is in this examples is typicaly less than 10.
And we simply need to construct metamodels predicting the scores of that selected PC.
The number was selected based on compromise between gained improvement and the difficulty to fit a GP metamodel.

## Slide 20: Testing the Trained Metamodel () on the Testing Samples ()
Observed Error [K]
Predicted Error [K]
Predicted Error [Pa]
Observed Error [Pa]
Observed Error [kg]
Predicted Error [kg]
Clad Temperature
Pressure Drop
Liquid Carryover
GP RMSE
Testing Samples
Acceptable metamodel predictive performance based on the testing samples
Notes: The metamodel prediction is limited by the error due to dimension reduction
It also shows that we cannot go better than the error given by the metamodel.
In context it is find for the time being as the prior uncertainty gives a larger error (standard deviation)

## Slide 21: Statistical Framework: Outline
Global Sensitivity Analysis
Gaussian Process Metamodeling
Bayesian Calibration
How to select important parameters to be inferred?
How to approximate the input/output of the forward model?
How to make the inference (quantification)?
27 initial parameters
12 influential parameters
Wide, independent prior uncertainties
Use experimental data to constrain the prior

## Slide 22: Bayesian Calibration, Inverse Quantification: Uncertain (Inputs + Data) Uncertain Inputs Updated
Forward Model
Uncertain model parameters (posterior)
Likelihood
Experimental Data from SETF
Additional sources of uncertainty
Uncertain model parameters (prior)
Controllable inputs (w.r.t experiment)
Probability of observing data given parameters
Bayes’
Theorem

## Slide 23: Two Aspects of Bayesian Calibration: Formulation and Computation
Forward Model
Uncertain model parameters (posterior)
Likelihood
Experimental Data from SETF
Additional sources of uncertainty
Uncertain model parameters (prior)
Controllable inputs (w.r.t experiment)
Formulation
Computation

## Slide 24: Formulation of Bayesian Calibration: True, Experimental, and Predicted Values
Model bias
Experimental data is a distorted information of the true value
Model prediction is a distorted information of the true value
Controlled variables (e.g., pressure, heat flux)
multi-dimensional data
measurement error,
Computer model
Given , what is the range of consistent ?
Model parameters

## Slide 25: Normal Likelihood and Flat Prior: Posterior Formulation
GP metamodel
Principal Comp. truncation
Model bias
measurement
Multiple sources of variance
Likelihood
GP
GP
Gaussian
given
Consider only data from one FEBA Test. No in formulation.
No | Calibration Schemes
1 | With all types of data
2 | against clad temperature (TC) data only
3 | against pressure drop (DP) data only
4 | against liquid carryover (CO) data only
5 | Without against all type of data
6 | excluding parameter
No | Calibration Schemes
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
unknown
6 calibration schemes were investigated
Notes: We will go through the main results provided by the first 4 schems
Note that no xc means we only deal with the calibration of the 8 model parameters.

## Slide 26: Computation of Bayesian Calibration
Bayes’ Theorem
Posterior
Likelihood
Prior
Uncertainty on is fully specified by , a multi-dimensional probability density function.
How to characterize? Use sampling.
The Metropolis-Hastings (MH) Algorithm to sample from the density :
Start at a random value of
Generate sample close to the current value
Accept or reject based on:
Joint
Marginal
Notes: MH in a nutshell
We actually use Ensemble MCMC
samples generated
Converge after of the way
MH in a nutshell
We actually use Ensemble MCMC
2×10^6 samples generated
Converge after 2/5 of the way

## Slide 27: Constraining the Prior Uncertainty Range of the Model Parameters
gridHT
iafbWHT
dffbWHT
dffbVIHT
iafbIntDr
dffbIntDr
dffbWDr
tQuench
The prior uncertainty of the model parameters
Notes: Can the data and the calibration model can be used to constrain this prior?

## Slide 28: Visualizing multi-dimensional distribution: How to read a corner plot?
gridHT
iafbWHT
dffbWHT
dffbVIHT
iafbIntDr
dffbIntDr
dffbWDr
tQuench
Bivariate Marginals
Joint plot of two parameters
Visualize pairwise correlations
Lighter color = high concentration of samples
Projection into one axis
Visualize the uncertainty of a parameter
Univariate Marginals
Notes: Can the data and the calibration model can be used to constrain this prior?

## Slide 29: Constraining the Prior Uncertainty Range of the Model Parameters
gridHT
iafbWHT
dffbWHT
dffbVIHT
iafbIntDr
dffbIntDr
dffbWDr
tQuench
The prior uncertainty of the model parameters
Notes: Can the data and the calibration model can be used to constrain this prior?

## Slide 30: Results: Considering pressure drop data to constrain the prior parameters range
gridHT
iafbWHT
dffbWHT
dffbVIHT
iafbIntDr
dffbIntDr
dffbWDr
tQuench
The posterior based on pressure drop data only
(samples)
Notes: The vertical lines in the diagonal is the 95% credible interval

## Slide 31: Results: Considering multiple types of data helps constrain the parameters uncertainty
gridHT
iafbWHT
dffbWHT
dffbVIHT
iafbIntDr
dffbIntDr
dffbWDr
tQuench
The posterior based on all types of data
(samples)
Notes: Data can help constrain the prior range of the model parameters. (only small part of the prior that is consistent with the calibration data)
But the posterior samples also exhibit correlation among the parameters

## Slide 32: Results: Posterior Samples are Correlated (i.e., a set of “collectively-fitted” values)
Time [s]
Clad Temperature [K]
Middle assembly
Top assembly
Uncertainty propagation on FEBA Test. No. 216 (the calibration data) based on 1’000 Monte Carlo samples.
Prior
Posterior, Correlated
Posterior, Independent
Notes: A set of “collectively-fitted” values which means that if we don’t consider them as a collection then the prediction would less match the calibration data itself.
If we only consider the univariate marginals (neglecting correlation) we obtain prediction that is less consistent with the calibration data.
Only if we consider the posterior samples jointly, that the prediction match the experimental data better.

## Slide 33: Statistical Framework: Outline
Global Sensitivity Analysis
Gaussian Process Metamodeling
Bayesian Calibration
How to select important parameters to be inferred?
How to approximate the input/output of the forward model?
How to make the inference (quantification)?
Is the quantified uncertainty useful?
27 initial parameters
12 influential parameters
Wide, independent prior uncertainties
Narrower, correlated posterior uncertainties
Uncertainty Propagation
Wide prior prediction uncertainties
Propagate posterior uncertainties for different experimental conditions

## Slide 34: Comparing Different Calibration Results: Informativeness vs. Calibration Score
Two scores to summarize and compare results of uncertainty propagation using different posterior samples w.r.t the prior
LUB: Lower Uncertainty Bound
( prediction percentile)
( prediction percentile)
UUB: Upper Uncertainty Bound
Informativeness for output
Posterior prediction uncertainty is equal to that of the prior
No posterior prediction uncertainty
Notes: Think of a posterior prediction is a source of information for output y and defined only in three values, the lower uncertainty bound, the upper uncertainty bound and the reference value
Informativeness tries to measure the width of posterior uncertainty band relative to that of the prior

## Slide 35: Comparing Different Calibration Results: Informativeness vs. Calibration Score
Two scores to summarize and compare results of uncertainty propagation using different posterior samples w.r.t the prior
Calibration Score for output
Experimental data falls outside the uncertainty band
Experimental data matches the reference value exactly
The height of the experimental data in the information triangle
: Reference value
( prediction percentile; median)
Notes: Calibration measure the location of experimental data inside the so called “information” triangle
The bottom line is this, large informativeness means narrower uncertainty band and large calibration means closer to experimental data, while lower often means the band covers less experimental data

## Slide 36: Posterior prediction uncertainties are narrower, but cover less experimental data
  ,
Calibration [-]
  ,
  ,
  ,
  ,
Calibration Scheme
Informativeness [-]
Notes: Across experimental conditions there is no strong pattern of discrepancy
Less “calibrated” here means cover less experimental data points
If we don’t consider correlation, the uncertainties
Yes the calibration score falls for all, but it is because fail to cover the experimental data by the band is highly penalizing. What we are interested in this comparison, especially to indicate whether the overfitting occurs severely is to look at the different prior and posterior calibration and compare with the results of Test 216. If the difference is larger than it would slightly overfit. There is no significant overfitting based on this difference.

## Slide 37: Removing highly Correlated parameter and keeping it at its prior range give a compromise
Calibration [-]
  ,
  ,
  ,
  ,
  ,
Calibration Scheme
Informativeness [-]
Notes: Yet there is reason to be prudent when it comes to correlation. (univariate marginal) Parameter uncertainty can be wide (indicating no overfitting) but the correlation can cause such overfitting nevertheless.

## Slide 38: Conclusion
Consolidation, implementation, and application of tools based on statistical framework for quantifying the physical model parameters in TRACE code
Motivation:
Objectives:
Contribution:
Given data from a separate effect test facility, develop a methodology to systematically quantify the uncertainty of the parameters in TRACE code
Global Sensitivity Analysis
Gaussian Process Metamodeling
Bayesian Calibration
Uncertainty Propagation
Uncertainty in physical model parameters are often derived solely based on expert-judgment and on a particular calibration data

## Slide 39: Contributions (1/2)
Motivation:
Developed Tools:
Contribution:

## Slide 40: Contributions (2/2): Demonstration of the Methodology on the FEBA TRACE Model
Global Sensitivity Analysis
Gaussian Process Metamodeling
Bayesian Calibration
How to select important parameters to be inferred?
How to approximate the input/output of the forward model?
How to make the inference (quantification)?
Is the quantified uncertainty useful?
27 initial parameters
12 influential parameters
Wide, independent prior uncertainties
Narrower, correlated posterior uncertainties
Uncertainty Propagation
Narrower posterior prediction uncertainties for all exp. conditions
Wide prior prediction uncertainties
Notes: FEBA TRACE model is a relatively small and simple model, but it is by no means a toy model. It illustrates a typical analysis of calibrating TRACE model parameters based on SETF

## Slide 41: Future Work
Global Sensitivity Analysis
Gaussian Process Metamodeling
PCA performed worse for reconstructing output with discontinuity. Need alternative dimension reduction method.
  Better
  Worse
Non-sensitive parameters are non-identifiable
Highly sensitivity parameters are identifiable
Unclear for parameters with intermediate sensitivity
Need to establish a connection between GSA and identifiability.
Notes: As for GP metamodeling, we are lucky because the error incurred by such imperfection is smaller than the overall initial variation induced by the prior uncertainty. But if the uncertainty becomes more precise, we need more accurate metamodeling approach, at least in dealing with output containing discontinuity. Basically the difference between 9 and 0.9% previously explained.

## Slide 42: Future Works
Bayesian Calibration
Uncertainty Propagation
  216
  214
How to summarize generic correlation structure of the posterior useful for downstream analysis? (Copula?)
Calibration was only done based on one dataset. Error structure might differ
Sequential calibration against other SETF remains open question
ACHILLES
RBHT
  220
  222
  223
  218
FEBA
Notes: We calibrate only with one (and we did verify against different test data), but its performance depends on the assume error structure that derived only with the aforementioned calibration data. We need to simultaneously consider
We don’t often consider correlation among model parameters, but calibration will result in a correlated posterior. Consistent propagation requires this information to be carried.
What is the repercussion in practice when we have to consider such correlation in the model parameters.

## Slide 43: Wir schaffen Wissen – heute für morgen
Thank you for your attention.
My sincere gratitude to:
Prof. A. Pautz
Mr. O. Zerkak
Dr. G. Perret
Mr. Ph. Jacquemoud
Dr. M. Hursin
Dr. D. Rochman
Mr. H. Ferroukhi
Other members of STARS
The jury members:
Dr. J. Baccou
Prof. R. Houdré
Prof. B. Sudret
Dr. W. Zwermann
Additional acknowledgments:
Swiss Federal Nuclear Safety Inspectorat (ENSI)
Swiss Federal Office of Energy (BFM)